## Slide 1
UNIT 5 · 9 hours
Summing Amplifier
Op-Amp and Linear IC Applications
Basic Electrical and Electronics Engineering (EEE103)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Summing Amplifier", part of Unit 5 (Op-Amp and Linear IC Applications) of Basic Electrical and Electronics Engineering.

## Slide 2: Learning objectives
U5
Draw an inverting summing amplifier
Derive the output expression
Design an averaging circuit
Solve numericals
Syllabus context
Introduction, op-amp specifications, differential and common-mode operation, op-amp applications: inverting/non-inverting amplifier, summing, integrator, differentiator, comparator, 555 timer IC in astable mode, 78XX series IC voltage regulators.
Notes: By the end of this topic you should be able to do the following. Draw an inverting summing amplifier. Derive the output expression. Design an averaging circuit. Solve numericals.

## Slide 3: Circuit and operation
U5
Several inputs v1, v2, v3 connected through R1, R2, R3 to the inverting node.
Non-inverting terminal grounded; feedback resistor Rf.
The inverting node is a virtual ground, so each input current is independent: i1 = v1/R1, etc.
KCL at the node: if = i1 + i2 + i3 and if = −vo/Rf.
Notes: The summing amplifier is an inverting amplifier with several input branches. Because the summing node is at virtual ground, the sources do not interact.

## Slide 4: Output expression
U5
vo = −[ (Rf/R1) v1 + (Rf/R2) v2 + (Rf/R3) v3 ]
weighted sum
R1 = R2 = R3 = R: vo = −(Rf/R)(v1 + v2 + v3)
scaled adder
Rf = R/3: vo = −(v1 + v2 + v3)/3
averager
Notes: If all resistors are equal the output is the negative of the sum.

## Slide 5: Numerical: adder
U5
Problem R1 = R2 = R3 = 10 kΩ, Rf = 10 kΩ; v1 = 1 V, v2 = 2 V, v3 = 3 V. Find vo.
vo = −(Rf/R)(v1 + v2 + v3)
= −(10/10)(1 + 2 + 3)
Answer: vo = −6 V
Notes: A positive sum gives a negative output; follow with an inverter if a positive output is needed.

## Slide 6: Numerical: weighted sum
U5
Problem R1 = 10 kΩ, R2 = 20 kΩ, R3 = 40 kΩ, Rf = 40 kΩ; inputs 1 V each. Find vo.
Gains: Rf/R1 = 4, Rf/R2 = 2, Rf/R3 = 1
vo = −(4 × 1 + 2 × 1 + 1 × 1)
Answer: vo = −7 V
Notes: This binary weighted resistor network is the idea behind a digital to analog converter.

## Slide 7: Applications
U5
Audio mixers: combine several channels.
Averaging circuits (Rf = R/n).
D/A converters using binary weighted resistors.
Analog computers: summation block.
Notes: The audio mixer is the classic application.

## Slide 8: Key takeaways
U5
vo = −(Rf/R1 v1 + Rf/R2 v2 + Rf/R3 v3)
Inputs do not interact because of the virtual ground
Equal R and Rf = R/n gives an inverting average
Basis of weighted-resistor DACs and mixers
Notes: To summarise this topic. vo = −(Rf/R1 v1 + Rf/R2 v2 + Rf/R3 v3). Inputs do not interact because of the virtual ground. Equal R and Rf = R/n gives an inverting average. Basis of weighted-resistor DACs and mixers.

## Slide 9: Practice questions
U5
Q1. Derive the output of a 3-input summing amplifier.
Q2. Design an averager of three inputs.
Q3. R = 10 kΩ, Rf = 20 kΩ, v1 = 0.5 V, v2 = 1 V: find vo.
Q4. Why do the sources not interact in the summing amplifier?
Notes: Attempt these on your own, then check your working against your notes and textbook. Derive the output of a 3-input summing amplifier. Design an averager of three inputs. R = 10 kΩ, Rf = 20 kΩ, v1 = 0.5 V, v2 = 1 V: find vo. Why do the sources not interact in the summing amplifier?