## Slide 1
UNIT 1 · 8 hours
Block Diagram Algebra and Reduction Techniques
Introduction and Mathematical Modelling of Physical Systems
Control Systems (22EEG53)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Block Diagram Algebra and Reduction Techniques", part of Unit 1 (Introduction and Mathematical Modelling of Physical Systems) of Control Systems.

## Slide 2: Learning objectives
U1
Identify block, summing point and take-off point
Apply series, parallel and feedback reduction rules
Shift summing and take-off points
Reduce a multi-loop block diagram to a single transfer function
Syllabus context
Introduction and mathematical modelling of physical systems: open loop and closed loop systems, examples, control system components. Transfer function of physical systems: mechanical systems (translational and rotational), electrical systems, analogous systems, block diagram reduction techniques, signal flow graphs.
Notes: By the end of this topic you should be able to do the following. Identify block, summing point and take-off point. Apply series, parallel and feedback reduction rules. Shift summing and take-off points. Reduce a multi-loop block diagram to a single transfer function.

## Slide 3: Elements of a block diagram
U1
Block: rectangle containing the transfer function; output = G × input.
Summing point: circle with ± signs; algebraic sum of signals.
Take-off point: dot: the same signal is branched off without loading.
Arrows: direction of signal flow.
Why reduce? to get one overall transfer function C(s)/R(s).
Notes: A block diagram gives a pictorial representation of the functional relationships among components.

## Slide 4: Rule 1: blocks in series (cascade)
U1
C/R = G1 · G2
Valid when blocks do not load each other.
Any number of blocks: multiply all.
Notes: The output of the first block is the input of the second.

## Slide 5: Rule 2: blocks in parallel
U1
C/R = G1 ± G2
Signs follow the summing point.
Same input to both blocks.
Notes: Outputs are added or subtracted at the summing point.

## Slide 6: Rule 3: feedback loop
U1
C/R = G / (1 ± GH)
Negative feedback: 1 + GH; positive: 1 − GH.
Unity feedback: H = 1 → G/(1 + G).
GH = open-loop transfer function.
Notes: This is the most used reduction.

## Slide 7: Moving summing and take-off points
U1
Operation | Rule
Move take-off point beyond a block G | Add a block G in the branch
Move take-off point before a block G | Add a block 1/G in the branch
Move summing point beyond a block G | Add G in the branch being moved
Move summing point before a block G | Add 1/G in the branch being moved
Interchange adjacent summing points | Allowed
Interchange summing and take-off points | Not allowed (shift across a block)
Notes: The aim of moving points is to expose simple series, parallel or feedback combinations.

## Slide 8: Reduction procedure
U1
1
Combine series
Multiply cascade blocks.
2
Combine parallel
Add/subtract blocks with common input and output.
3
Eliminate inner loops
Apply G/(1 ± GH) to the innermost feedback.
4
Shift points
Only when needed to untangle.
5
Repeat
Until a single block remains.
Rule of thumb: reduce inner loops first and keep the same input/output.
Notes: Work from the inside out. Always check signs at the summing points.

## Slide 9: Example: multi-loop diagram
U1
Inner loop: G2 G3 with feedback H1.
Then outer loop: G1 with feedback H2 taken after G2.
Reduce step by step.
Notes: Here H1 feeds back from the output to the second summing point, and H2 feeds back from the output of G2 to the first summing point.

## Slide 10: Reducing the example
U1
Problem G1 = 10, G2 = 2, G3 = 5, H1 = 0.1, H2 = 0.2. Find C/R.
Inner loop (G2G3 with H1): G2G3/(1 + G2G3H1) = 10/(1 + 1) = 5
Path u1 → G2 output: G2/(1 + G2G3H1) = 2/2 = 1
Overall: C/R = G1G2G3 / (1 + G2G3H1 + G1G2H2)
= 100 / (1 + 1 + 4)
Answer: C/R = 100/6 = 16.67
Notes: Verify by symbolic reduction: the denominator contains one term per loop.

## Slide 11: Key takeaways
U1
Series: G1G2; parallel: G1 ± G2; feedback: G/(1 ± GH)
Move take-off points and summing points to expose simple forms
Reduce inner loops first
Check signs at every summing point
Notes: To summarise this topic. Series: G1G2; parallel: G1 ± G2; feedback: G/(1 ± GH). Move take-off points and summing points to expose simple forms. Reduce inner loops first. Check signs at every summing point.

## Slide 12: Practice questions
U1
Q1. Reduce a unity-feedback system with G = 10/(s(s+2)) to a single block.
Q2. State the rules for shifting a take-off point across a block.
Q3. G1 = 1/(s+1), G2 = 1/(s+2), H = 1: find C/R.
Q4. Why can't a summing point and a take-off point be interchanged directly?
Notes: Attempt these on your own, then check your working against your notes and textbook. Reduce a unity-feedback system with G = 10/(s(s+2)) to a single block. State the rules for shifting a take-off point across a block. G1 = 1/(s+1), G2 = 1/(s+2), H = 1: find C/R. Why can't a summing point and a take-off point be interchanged directly?