## Slide 1
UNIT 2 · 8 hours
Type of Systems and Static Error Constants
Time Domain Analysis of Control Systems
Control Systems (22EEG53)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Type of Systems and Static Error Constants", part of Unit 2 (Time Domain Analysis of Control Systems) of Control Systems.

## Slide 2: Learning objectives
U2
Define the type of a system
Define position, velocity and acceleration error constants
Compute steady-state error for step, ramp and parabolic inputs
Relate type to error
Syllabus context
Time domain analysis of control systems: standard test signals, time response of zero, first and second order systems, time domain specifications, type of systems, static error constants and steady-state error, generalized error series.
Notes: By the end of this topic you should be able to do the following. Define the type of a system. Define position, velocity and acceleration error constants. Compute steady-state error for step, ramp and parabolic inputs. Relate type to error.

## Slide 3: Type of a system
U2
G(s)H(s) = K Π(1 + Tz s) / [ s^N Π(1 + Tp s) ]
open-loop transfer function
Type = N
number of poles at s = 0
Error: e(t) = r(t) − c(t)
unity feedback
Type 0: no pole at the origin; type 1: one (an integrator); type 2: two.
Type, not order, determines steady-state accuracy.
Notes: The type is the number of integrations in the open loop transfer function.

## Slide 4: Static error constants
U2
Constant | Definition | Input
Position Kp | lim s→0 G(s)H(s) | Step
Velocity Kv | lim s→0 s G(s)H(s) | Ramp
Acceleration Ka | lim s→0 s² G(s)H(s) | Parabola
Notes: These constants measure the ability of the system to track step, ramp and parabolic inputs.

## Slide 5: Steady-state error: unity feedback
U2
Type | Step (1) | Ramp (t) | Parabola (t²/2)
0 | 1/(1 + Kp) | ∞ | ∞
1 | 0 | 1/Kv | ∞
2 | 0 | 0 | 1/Ka
3 | 0 | 0 | 0
ess = lim s→0 s R(s)/(1 + G(s)): valid only for a stable closed-loop system.
Notes: Increasing the type reduces the error, but makes the system harder to stabilise.

## Slide 6: Numerical 1: type 1 system
U2
Problem Unity feedback with G(s) = 10/[s(s + 2)]. Find type, Kp, Kv, Ka and ess for unit step, unit ramp.
Type 1 (one pole at origin)
Kp = ∞; Kv = lim s·G = 10/2 = 5; Ka = 0
ess (step) = 0; ess (ramp) = 1/Kv = 0.2
Answer: Type 1; Kv = 5; ess = 0 (step), 0.2 (unit ramp)
Notes: A type 1 system tracks a step exactly but lags a ramp.

## Slide 7: Numerical 2: type 0 and type 2
U2
Problem (a) G = 20/[(s+1)(s+4)]; (b) G = 10(s+1)/[s²(s+4)], unity feedback. Find the error for a unit step (a) and a unit parabola (b).
(a) Type 0: Kp = 20/4 = 5 ⇒ ess = 1/(1 + 5) = 0.167
(b) Type 2: Ka = lim s²G = 10(1)/4 = 2.5
ess (parabola) = 1/Ka = 0.4; ess (ramp) = 0
Answer: (a) 0.167; (b) 0.4
Notes: Remember to take the limit after cancelling the s terms.

## Slide 8: Remarks
U2
Unity feedback assumed; for H ≠ 1 use e = r − b or the actuating error carefully.
K enters the constants: a larger gain gives a smaller error.
Stability limits how large K can be: accuracy versus stability trade-off.
Compensators (Unit 5) improve accuracy without destroying stability.
Notes: A higher type or larger gain improves accuracy, but there is a limit set by stability.

## Slide 9: Key takeaways
U2
Type = number of poles at the origin of G(s)H(s)
Kp = lim G; Kv = lim sG; Ka = lim s²G
ess = 1/(1 + Kp), 1/Kv, 1/Ka for step, ramp, parabola
Higher type ⇒ lower error but harder stability
Notes: To summarise this topic. Type = number of poles at the origin of G(s)H(s). Kp = lim G; Kv = lim sG; Ka = lim s²G. ess = 1/(1 + Kp), 1/Kv, 1/Ka for step, ramp, parabola. Higher type ⇒ lower error but harder stability.

## Slide 10: Practice questions
U2
Q1. Define Kp, Kv and Ka.
Q2. G = 50/[s(s+5)(s+10)]: find Kv and ramp error.
Q3. A type 0 system has Kp = 9: find the step error.
Q4. Tabulate steady-state error versus type.
Notes: Attempt these on your own, then check your working against your notes and textbook. Define Kp, Kv and Ka. G = 50/[s(s+5)(s+10)]: find Kv and ramp error. A type 0 system has Kp = 9: find the step error. Tabulate steady-state error versus type.