## Slide 1
UNIT 4 · 8 hours
Routh–Hurwitz Stability Criterion
Stability of Systems
Control Systems (22EEG53)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Routh–Hurwitz Stability Criterion", part of Unit 4 (Stability of Systems) of Control Systems.

## Slide 2: Learning objectives
U4
Construct the Routh array
State the necessary and sufficient condition
Handle a zero in the first column and a row of zeros
Find the range of K for stability and the marginal frequency
Syllabus context
Stability of systems: characteristic equation, location of roots, absolute and relative stability, Routh–Hurwitz criterion (necessary and sufficient conditions), root locus concept, rules for construction of root locus.
Notes: By the end of this topic you should be able to do the following. Construct the Routh array. State the necessary and sufficient condition. Handle a zero in the first column and a row of zeros. Find the range of K for stability and the marginal frequency.

## Slide 3: Constructing the Routh array
U4
1
Write polynomial
a0sⁿ + a1sⁿ⁻¹ + a2sⁿ⁻² + … (a0 > 0).
2
First two rows
Row sⁿ: a0, a2, a4 …; row sⁿ⁻¹: a1, a3, a5 …
3
Next rows
b1 = (a1a2 − a0a3)/a1, b2 = (a1a4 − a0a5)/a1, …
4
Continue
Each element = (pivot × element above-right − element above × pivot-right)/pivot.
Condition: all roots in the LHP ⇔ no sign change in the first column; sign changes = number of RHP roots.
Notes: Continue until the row for s to the power zero is reached. Rows get shorter as you go down.

## Slide 4: Example 1: stable
U4
Problem s³ + 6s² + 11s + 6 = 0. Is the system stable?
s³: 1 11
s²: 6 6
s¹: (6×11 − 1×6)/6 = 10
s⁰: 6
First column 1, 6, 10, 6: no sign change
Answer: Stable (roots −1, −2, −3)
Notes: All elements in the first column are positive.

## Slide 5: Example 2: unstable
U4
Problem s⁴ + 2s³ + 3s² + 4s + 5 = 0. How many roots are in the RHP?
s⁴: 1 3 5
s³: 2 4
s²: (2×3 − 1×4)/2 = 1, (2×5 − 0)/2 = 5
s¹: (1×4 − 2×5)/1 = −6
s⁰: 5. First column 1, 2, 1, −6, 5: two sign changes
Answer: Unstable: 2 roots in the RHP
Notes: The number of sign changes in the first column gives the number of roots in the right half plane.

## Slide 6: Example 3: range of K
U4
Problem Unity feedback, G = K/[s(s + 1)(s + 2)]. Find the range of K for stability and the oscillation frequency at the limit.
Characteristic: s³ + 3s² + 2s + K = 0
s³: 1 2; s²: 3 K; s¹: (6 − K)/3; s⁰: K
Stable: (6 − K)/3 > 0 and K > 0 ⇒ 0 < K < 6
K = 6: auxiliary 3s² + 6 = 0 ⇒ s = ± j√2
Answer: 0 < K < 6; marginal oscillation at ω = 1.414 rad/s
Notes: This matches the gain margin of nine point five four dB found for K equals two.

## Slide 7: Special case 1: zero in the first column
U4
Problem
A zero appears in the first column with other non-zero elements in the row.
Remedy
Replace 0 by a small ε > 0, continue, then let ε → 0 and count sign changes.
Example
s⁴ + s³ + 2s² + 2s + 3: s²-row first element ε; s¹ element → −3/ε (negative): two sign changes ⇒ 2 RHP roots.
Notes: An alternative is to substitute s equals one over z and apply the test again.

## Slide 8: Special case 2: a row of zeros
U4
Problem
An entire row is zero: the polynomial has roots symmetric about the origin.
Remedy
Form the auxiliary polynomial A(s) from the row above; replace the zero row by dA/ds coefficients.
Example
s³ + 2s² + s + 2: s¹ row zero; A(s) = 2s² + 2 ⇒ roots ± j1; no sign change ⇒ marginally stable.
Notes: The roots of the auxiliary polynomial are roots of the original polynomial.

## Slide 9: Key takeaways
U4
Routh array: no sign change in the first column ⇒ stable
Number of sign changes = number of RHP roots
Zero in first column: use ε; row of zeros: use the auxiliary polynomial
Range of K from the s¹ and s⁰ entries
Notes: To summarise this topic. Routh array: no sign change in the first column ⇒ stable. Number of sign changes = number of RHP roots. Zero in first column: use ε; row of zeros: use the auxiliary polynomial. Range of K from the s¹ and s⁰ entries.

## Slide 10: Practice questions
U4
Q1. Apply Routh's test to s⁴ + 8s³ + 18s² + 16s + 5.
Q2. Find K for stability: s³ + 5s² + 6s + K = 0.
Q3. Apply Routh to s⁵ + s⁴ + 3s³ + 3s² + 2s + 2 and explain the zero row.
Q4. What does the auxiliary equation represent?
Notes: Attempt these on your own, then check your working against your notes and textbook. Apply Routh's test to s⁴ + 8s³ + 18s² + 16s + 5. Find K for stability: s³ + 5s² + 6s + K = 0. Apply Routh to s⁵ + s⁴ + 3s³ + 3s² + 2s + 2 and explain the zero row. What does the auxiliary equation represent?