## Slide 1
UNIT 5 · 9 hours
Op-Amp Specifications
Op-Amp and Linear IC Applications
Basic Electrical and Electronics Engineering (EEE103)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Op-Amp Specifications", part of Unit 5 (Op-Amp and Linear IC Applications) of Basic Electrical and Electronics Engineering.

## Slide 2: Learning objectives
U5
Define key op-amp specifications
Interpret typical values for the 741
Calculate slew-rate limits
Understand offset voltage and bias currents
Syllabus context
Introduction, op-amp specifications, differential and common-mode operation, op-amp applications: inverting/non-inverting amplifier, summing, integrator, differentiator, comparator, 555 timer IC in astable mode, 78XX series IC voltage regulators.
Notes: By the end of this topic you should be able to do the following. Define key op-amp specifications. Interpret typical values for the 741. Calculate slew-rate limits. Understand offset voltage and bias currents.

## Slide 3: Important specifications
U5
Parameter | Definition | 741 typical
Input offset voltage | Differential input needed to make output zero | 2 mV
Input bias current | Average of the two input currents | 80 nA
Input offset current | Difference of the two input currents | 20 nA
CMRR | Ad / Acm | 90 dB
PSRR | ΔVsupply / ΔVout (input referred) | 30 µV/V
Slew rate | Maximum dVo/dt | 0.5 V/µs
Output swing | Max undistorted peak output | ±13 V
Notes: These are datasheet parameters used when selecting an op amp.

## Slide 4: Input-related specifications
U5
Input impedance
Ratio of input voltage change to input current change at one terminal. Very high (MΩ–TΩ).
Input offset voltage
Ideally both inputs grounded → vo = 0. In practice a small offset appears; a differential voltage must be applied to null it.
Input bias and offset currents
Small DC currents flowing into the input transistors; cause output errors with high-value resistors.
Notes: Offset voltage and bias currents cause a small non zero output with zero input.

## Slide 5: Output and frequency specifications
U5
Output impedance
Ratio of output voltage change to output current change; low (≈ 75 Ω for the 741).
Output voltage swing
Peak output without distortion; slightly less than the supply: ±13 V on ±15 V.
Bandwidth and slew rate
Gain-bandwidth product ≈ 1 MHz; slew rate = speed limit of the output.
Notes: Slew rate limits the large-signal bandwidth.

## Slide 6: Slew rate and CMRR formulas
U5
SR = (dVo/dt)max
V/µs
fmax = SR / (2π Vp)
full-power bandwidth
CMRR = Ad / Acm
in dB: 20 log10(Ad/Acm)
For a sine of peak Vp, (dVo/dt)max = 2π f Vp.
Notes: If the signal demands a faster change than the slew rate, the output becomes distorted.

## Slide 7: Numerical: slew-rate limit
U5
Problem A 741 (SR = 0.5 V/µs) amplifies a sine of peak output 10 V. What is the highest undistorted frequency?
fmax = SR / (2π Vp)
= 0.5 × 10⁶ V/s / (2π × 10 V)
Answer: fmax ≈ 7.96 kHz
Notes: Beyond this frequency the sine becomes a triangle wave.

## Slide 8: Key takeaways
U5
Offset voltage and bias currents cause output errors
CMRR = Ad/Acm (often in dB)
Slew rate limits output speed: fmax = SR/(2πVp)
741: ±13 V swing, 1 MHz, 0.5 V/µs
Notes: To summarise this topic. Offset voltage and bias currents cause output errors. CMRR = Ad/Acm (often in dB). Slew rate limits output speed: fmax = SR/(2πVp). 741: ±13 V swing, 1 MHz, 0.5 V/µs.

## Slide 9: Practice questions
U5
Q1. Define input offset voltage and bias current.
Q2. Find the maximum frequency for a 5 V peak output with SR = 1 V/µs.
Q3. Define CMRR and slew rate.
Q4. What limits the large-signal bandwidth of an op-amp?
Notes: Attempt these on your own, then check your working against your notes and textbook. Define input offset voltage and bias current. Find the maximum frequency for a 5 V peak output with SR = 1 V/µs. Define CMRR and slew rate. What limits the large-signal bandwidth of an op-amp?