## Slide 1
UNIT 5 · 9 hours
Differential and Common-Mode Operation
Op-Amp and Linear IC Applications
Basic Electrical and Electronics Engineering (EEE103)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Differential and Common-Mode Operation", part of Unit 5 (Op-Amp and Linear IC Applications) of Basic Electrical and Electronics Engineering.

## Slide 2: Learning objectives
U5
Explain single-ended, differential and common-mode operation
Define differential and common-mode gain
Calculate CMRR in ratio and dB
Explain the concept of virtual ground
Syllabus context
Introduction, op-amp specifications, differential and common-mode operation, op-amp applications: inverting/non-inverting amplifier, summing, integrator, differentiator, comparator, 555 timer IC in astable mode, 78XX series IC voltage regulators.
Notes: By the end of this topic you should be able to do the following. Explain single-ended, differential and common-mode operation. Define differential and common-mode gain. Calculate CMRR in ratio and dB. Explain the concept of virtual ground.

## Slide 3: Modes of operation
U5
Single-ended
One input is grounded (v1 = 0 or v2 = 0). Output = A × other input.
Differential mode
Inputs equal and opposite (v1 = −v2). Output = Ad (v2 − v1).
Common mode
Inputs identical (v1 = v2 = vcm). Ideal output = 0; practical output = Acm vcm.
Notes: Op amps respond mainly to the difference between inputs.

## Slide 4: Output equation
U5
vo = Ad vd + Acm vcm
general
vd = v2 − v1
difference
vcm = (v1 + v2)/2
average
Ideal op-amp: Acm = 0, so vo depends only on vd.
Practical: small Acm ≠ 0 → noise common to both inputs leaks to the output.
Notes: The output of a practical op amp has two components.

## Slide 5: CMRR
U5
CMRR = Ad / Acm
ratio
CMRR (dB) = 20 log10 (Ad / Acm)
decibels
High CMRR means good rejection of common noise: hum, interference picked up equally on both leads.
741: 70–90 dB typical.
Essential in instrumentation amplifiers and sensor circuits.
Notes: The relative sensitivity of an op amp to a difference signal as compared to a common mode signal is the C M R R.

## Slide 6: Numerical: CMRR and output
U5
Problem An op-amp has Ad = 10⁵ and Acm = 1. Find CMRR in dB. For v1 = 100.0 mV and v2 = 100.1 mV find the output.
CMRR = 10⁵/1 = 10⁵ → 20 log10(10⁵) = 100 dB
vd = 0.1 mV; vcm = 100.05 mV
vo = 10⁵ × 0.1 mV + 1 × 100.05 mV = 10 V + 0.1 V
Answer: CMRR = 100 dB; vo ≈ 10.1 V (0.1 V error from common mode)
Notes: The common mode component contributes about one percent of the output.

## Slide 7: Virtual ground
U5
Output is limited by the supply, e.g. |vo| ≤ 13 V, while A ≈ 10⁵.
So the input difference vd = vo/A is tiny (e.g. 5 V/5000 = 1 mV in closed loop).
Virtual short: v1 ≈ v2. If the non-inverting input is grounded, the inverting input is at 0 V: virtual ground.
No current flows into the op-amp terminals: it is a virtual short, not a real one.
Notes: A virtual short circuit exists between the two input terminals even though no current passes through it.

## Slide 8: Key takeaways
U5
vo = Ad vd + Acm vcm
CMRR = Ad/Acm; in dB = 20 log10
High CMRR rejects noise common to both inputs
Virtual ground: v1 ≈ v2 with no input current
Notes: To summarise this topic. vo = Ad vd + Acm vcm. CMRR = Ad/Acm; in dB = 20 log10. High CMRR rejects noise common to both inputs. Virtual ground: v1 ≈ v2 with no input current.

## Slide 9: Practice questions
U5
Q1. Explain the three modes of op-amp operation.
Q2. Ad = 2000, Acm = 0.2. Find CMRR in dB.
Q3. What is virtual ground and why does it occur?
Q4. Why is high CMRR important for sensor signals?
Notes: Attempt these on your own, then check your working against your notes and textbook. Explain the three modes of op-amp operation. Ad = 2000, Acm = 0.2. Find CMRR in dB. What is virtual ground and why does it occur? Why is high CMRR important for sensor signals?