## Slide 1
UNIT 2 · 8 hours
Steady-State Error and Generalized Error Series
Time Domain Analysis of Control Systems
Control Systems (22EEG53)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Steady-State Error and Generalized Error Series", part of Unit 2 (Time Domain Analysis of Control Systems) of Control Systems.

## Slide 2: Learning objectives
U2
Use the final value theorem to find steady-state error
Explain the limitations of the static error constants
Derive the generalized error coefficients
Evaluate the error series for polynomial inputs
Syllabus context
Time domain analysis of control systems: standard test signals, time response of zero, first and second order systems, time domain specifications, type of systems, static error constants and steady-state error, generalized error series.
Notes: By the end of this topic you should be able to do the following. Use the final value theorem to find steady-state error. Explain the limitations of the static error constants. Derive the generalized error coefficients. Evaluate the error series for polynomial inputs.

## Slide 3: Steady-state error
U2
E(s) = R(s) / [1 + G(s)H(s)]
error signal
ess = lim s→0 s E(s)
final value theorem
Valid only if sE(s) has no poles on the jω axis or in the RHP (stable closed loop).
Depends on both the system type and the input.
Static error constants cover only step, ramp and parabola.
Notes: Apply the final value theorem to the error transform.

## Slide 4: Limitations of static constants
U2
They give only the final value of the error: a constant, zero or infinity.
They cannot tell how the error varies with time when it is infinite.
They cannot handle other inputs such as r(t) = 1 + t + t²/2 or sinusoids in a simple way.
The generalized error series expresses the steady-state error as a function of time.
Notes: The error series extends the static error constant idea.

## Slide 5: Generalized error coefficients
U2
1
Error transfer function
E(s)/R(s) = 1/(1 + G(s)H(s)) = We(s).
2
Expand
We(s) = C0 + C1 s + (C2/2!) s² + (C3/3!) s³ + …
3
Coefficients
Ci = d^i We(s)/ds^i at s = 0.
4
Error series
e_ss(t) = C0 r(t) + C1 ṙ(t) + (C2/2!) r̈(t) + …
C0, C1, C2 are the dynamic error coefficients: C0 = 1/(1 + Kp), C1 = 1/Kv, C2 = 1/Ka for the usual cases.
Notes: The coefficients are computed by long division of the error transfer function in ascending powers of s.

## Slide 6: Numerical: error series for a type 1 system
U2
Problem G = 10/[s(s + 2)], unity feedback. Find C0, C1, C2 and the steady-state error for r(t) = 1 + t + t²/2.
We = s(s + 2)/(s² + 2s + 10) = 0.2 s + 0.06 s² + …
C0 = 0; C1 = 0.2 (= 1/Kv); C2/2! = 0.06 ⇒ C2 = 0.12
r = 1 + t + t²/2; ṙ = 1 + t; r̈ = 1
e_ss(t) = 0 + 0.2(1 + t) + 0.06 × 1
Answer: e_ss(t) = 0.26 + 0.2 t (grows linearly: parabolic input unfollowed)
Notes: The error grows because the type 1 system cannot follow an accelerating input.

## Slide 7: Numerical: final value theorem
U2
Problem Unity-feedback system with G = 100/[s(s + 10)]. Find the error for a unit ramp using the final value theorem.
E(s) = R/(1 + G) = (1/s²) · s(s + 10)/(s² + 10s + 100) = (s + 10)/[s (s² + 10s + 100)]
s E(s) = (s + 10)/(s² + 10s + 100)
ess = lim s→0 sE(s) = 10/100
Answer: ess = 0.1 (= 1/Kv, Kv = 10)
Notes: Check: Kv equals G times s as s goes to zero, one hundred over ten.

## Slide 8: Effect of disturbances and design
U2
Disturbance error
A load disturbance D(s) adds an error; integral action before the disturbance entry point removes a constant disturbance error.
Increase gain K
Reduces the error but may reduce the damping.
Add integrator (type + 1)
Eliminates a constant error: PI controller, lag compensator (Unit 5).
Notes: Steady-state accuracy is improved by increasing the loop gain or adding integration.

## Slide 9: Key takeaways
U2
ess = lim s→0 sR(s)/(1 + GH) for a stable system
Static constants cover only step/ramp/parabola
Error series: e_ss = C0 r + C1 ṙ + (C2/2!) r̈ + …
Higher gain or integration improves accuracy
Notes: To summarise this topic. ess = lim s→0 sR(s)/(1 + GH) for a stable system. Static constants cover only step/ramp/parabola. Error series: e_ss = C0 r + C1 ṙ + (C2/2!) r̈ + …. Higher gain or integration improves accuracy.

## Slide 10: Practice questions
U2
Q1. Use the final value theorem for G = 20/[s(s+4)], unit ramp.
Q2. Find C0, C1, C2 for G = 5/[s(s + 1)].
Q3. Why must the closed loop be stable before applying the final value theorem?
Q4. Write the generalized error series.
Notes: Attempt these on your own, then check your working against your notes and textbook. Use the final value theorem for G = 20/[s(s+4)], unit ramp. Find C0, C1, C2 for G = 5/[s(s + 1)]. Why must the closed loop be stable before applying the final value theorem? Write the generalized error series.