## Slide 1
UNIT 5 · 8 hours
Introduction to Compensators
Compensators, Controllers and State-Space Analysis
Control Systems (22EEG53)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Introduction to Compensators", part of Unit 5 (Compensators, Controllers and State-Space Analysis) of Control Systems.

## Slide 2: Learning objectives
U5
Explain why compensation is needed
Describe series, feedback and feed-forward compensation
Compare lead, lag and lag-lead compensators
Choose a compensator type for a given deficiency
Syllabus context
Compensators and controllers: introduction to compensators, lag, lead and lag-lead compensators, P, PI and PID controllers.
Notes: By the end of this topic you should be able to do the following. Explain why compensation is needed. Describe series, feedback and feed-forward compensation. Compare lead, lag and lag-lead compensators. Choose a compensator type for a given deficiency.

## Slide 3: Why adjust gain is not enough
U5
Problem Unity feedback G = K/[s(s + 2)]. Required Kv = 20. What are ζ and Mp with this gain?
Kv = K/2 = 20 ⇒ K = 40
ωn = √40 = 6.32 rad/s; ζ = 2/(2 × 6.32) = 0.158
Mp = exp(−π × 0.158/√(1 − 0.025)) = 60.5 %
Answer: Accuracy is met but overshoot ≈ 60 %: a compensator is needed
Notes: Increasing gain to improve accuracy has reduced damping so much that the transient is unacceptable.

## Slide 4: Compensation
U5
Definition: adding extra components (compensator) to reshape the system so that specifications are met.
Specifications: steady-state accuracy, transient response (Mp, ts), stability margins (GM, PM), bandwidth.
Reasons: gain adjustment alone cannot satisfy conflicting requirements.
Design domains: root locus (s-plane) or Bode (frequency domain).
Notes: A compensator modifies the open loop transfer function to improve performance.

## Slide 5: Types of compensation
U5
Series (cascade)
Compensator Gc(s) placed in the forward path before the plant. Most common and simplest.
Feedback (parallel)
Compensator in the feedback path, e.g. tachometer (velocity) feedback; reduces effect of plant variations.
Feed-forward
Compensator acts on the reference or disturbance ahead of the loop; improves tracking or rejects measurable disturbances.
Notes: Most designs in this course use series compensation.

## Slide 6: Lead, lag and lag-lead at a glance
U5
Compensator | Form | Effect
Lead | (1 + aTs)/(1 + Ts), a > 1 | Adds phase lead: ↑ PM, ↑ bandwidth, faster response
Lag | (1 + Ts)/(1 + βTs), β > 1 | Cuts high-frequency gain: ↑ steady-state accuracy, ↓ bandwidth
Lag-lead | Lead × lag | Both: better accuracy and transient
P, PI, PID | Kp, Kp(1 + 1/Tis), … | Controllers: proportional, integral, derivative action
Notes: Choose the compensator that fixes the main deficiency.

## Slide 7: Lag and lead RC networks
U5
Lag network: Gc = (1 + sR2C)/[1 + s(R1 + R2)C].
Lead network: Gc = (1/a)(1 + aTs)/(1 + Ts), a = (R1 + R2)/R2, T = R1R2C/(R1 + R2).
Both are passive: attenuate at some frequencies.
Gain loss recovered by an amplifier.
Notes: These are the networks you will build in the lab.

## Slide 8: Key takeaways
U5
Compensators reshape the loop to meet specifications
Series, feedback and feed-forward compensation
Lead: transient; lag: steady-state accuracy; lag-lead: both
RC networks implement lead and lag
Notes: To summarise this topic. Compensators reshape the loop to meet specifications. Series, feedback and feed-forward compensation. Lead: transient; lag: steady-state accuracy; lag-lead: both. RC networks implement lead and lag.

## Slide 9: Practice questions
U5
Q1. Why is gain adjustment alone often inadequate?
Q2. Compare series and feedback compensation.
Q3. Which compensator improves steady-state error? Which improves PM?
Q4. Write the transfer functions of RC lag and lead networks.
Notes: Attempt these on your own, then check your working against your notes and textbook. Why is gain adjustment alone often inadequate? Compare series and feedback compensation. Which compensator improves steady-state error? Which improves PM? Write the transfer functions of RC lag and lead networks.