## Slide 1
UNIT 1 · 9 hours
Power and Energy
Circuit Fundamentals
Basic Electrical and Electronics Engineering (EEE103)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Power and Energy", part of Unit 1 (Circuit Fundamentals) of Basic Electrical and Electronics Engineering.

## Slide 2: Learning objectives
U1
Define electrical power and energy with units
Use P = VI, I²R and V²/R
Convert between joule, watt-hour and kilowatt-hour
Compute energy consumed and its cost
Syllabus context
Basic nodal and mesh analysis excited by independent DC voltage sources, Power and Energy. Generation of sinusoidal voltage, frequency, average value, RMS value, form factor and peak factor, phasor representation of alternating quantities.
Notes: By the end of this topic you should be able to do the following. Define electrical power and energy with units. Use P = VI, I²R and V²/R. Convert between joule, watt-hour and kilowatt-hour. Compute energy consumed and its cost.

## Slide 3: Power and energy: definitions
U1
Energy (U)
Capacity to do work. Unit: joule (J). Electrical energy: watt-hour (Wh), kilowatt-hour (kWh).
Power (P)
Rate of doing work: P = U / t.
Unit: watt, 1 W = 1 J/s.
Conversions
1 J = 1 W·s
1 Wh = 3600 J
1 kWh = 3.6 MJ = 1 'unit'
Notes: Power tells you how fast energy is converted; energy is power accumulated over time.

## Slide 4: Electrical power formulas
U1
P = V I
from V = W/Q and I = Q/t
P = I² R
substitute V = I R
P = V² / R
substitute I = V / R
Power is absorbed by a load (resistor) and delivered by a source.
I²R is the heating loss in conductors; it grows with the square of the current.
Notes: Derivation: power equals energy over time, which equals charge times voltage over time, which is V times I.

## Slide 5: Example 1: DC motor rating
U1
Problem A 24 V DC motor has a rated current of 33.5 A. What electrical power does it take?
P = V × I
P = 24 × 33.5
Answer: P = 804 W
Notes: A direct application of P equals V I.

## Slide 6: Example 2: energy of a lamp
U1
Problem How much energy (kWh) is needed to light a 60 W bulb continuously for 1 year (365 days)?
Time t = 365 × 24 = 8760 h
U = P × t = 60 × 8760 = 525 600 Wh
Convert to kWh: divide by 1000
Answer: U = 525.6 kWh
Notes: Energy is power times time. Multiply by the tariff to get the cost of electricity.

## Slide 7: Example 3: cost of running a heater
U1
Problem A 2 kW heater runs 3 h per day for 30 days. Tariff ₹6 per unit. Find energy and cost.
Energy = 2 kW × 3 h × 30 = 180 kWh (units)
Cost = 180 × 6
Answer: 180 kWh, ₹1080
Notes: One unit on the electricity bill is one kilowatt hour.

## Slide 8: Power in a source-resistor circuit
U1
Power delivered by sources = power absorbed by resistors (conservation of energy).
Check: mesh example, 10 V source gives 19.64 W; 18 Ω absorbs 3.59 W; the rest is absorbed by 1 Ω and 2 Ω and the 5 V source.
Source power: P = E·I; it can be negative if the current flows into the + terminal (the source is charging).
Always verify the power balance after solving a network.
Notes: A good check of any solved circuit is to confirm that total delivered power equals total absorbed power.

## Slide 9: Key takeaways
U1
P = VI = I²R = V²/R (watts)
Energy = power × time; 1 Wh = 3600 J; 1 kWh = 1 unit
Power delivered = power absorbed in a circuit
Heating loss varies as the square of the current
Notes: To summarise this topic. P = VI = I²R = V²/R (watts). Energy = power × time; 1 Wh = 3600 J; 1 kWh = 1 unit. Power delivered = power absorbed in a circuit. Heating loss varies as the square of the current.

## Slide 10: Practice questions
U1
Q1. A 230 V, 1 kW iron is used for 2 h. Find energy and current.
Q2. Find the resistance of a 100 W, 230 V lamp.
Q3. How many kWh does a 5 W LED bulb use in a year if on for 6 h/day?
Q4. Why does doubling current quadruple the conductor loss?
Notes: Attempt these on your own, then check your working against your notes and textbook. A 230 V, 1 kW iron is used for 2 h. Find energy and current. Find the resistance of a 100 W, 230 V lamp. How many kWh does a 5 W LED bulb use in a year if on for 6 h/day? Why does doubling current quadruple the conductor loss?