## Slide 1
UNIT 3 · 7 hours
Correlation Between Time and Frequency Responses
Frequency Domain Analysis
Control Systems (22EEG53)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Correlation Between Time and Frequency Responses", part of Unit 3 (Frequency Domain Analysis) of Control Systems.

## Slide 2: Learning objectives
U3
Relate Mp and Mr through ζ
Relate bandwidth to rise and settling time
Relate phase margin to damping ratio
Estimate time-domain performance from frequency plots
Syllabus context
Frequency domain analysis: frequency domain specifications peak resonance, resonant frequency, bandwidth and cut-off rate; correlation between time and frequency responses for second-order systems; Bode plot, gain margin and phase margin.
Notes: By the end of this topic you should be able to do the following. Relate Mp and Mr through ζ. Relate bandwidth to rise and settling time. Relate phase margin to damping ratio. Estimate time-domain performance from frequency plots.

## Slide 3: Why correlate?
U3
Both responses are determined by the same parameters ωn and ζ.
Frequency tests are easy; time-domain specs are what the user cares about.
For a second-order (or dominant second-order) system exact formulas relate them.
Design may be done in either domain.
Notes: The frequency response and the time response are two views of the same system.

## Slide 4: Peak overshoot Mp versus resonant peak Mr
U3
ζ | Mr | Mp (%)
0.2 | 2.55 | 52.7
0.3 | 1.75 | 37.2
0.4 | 1.36 | 25.4
0.5 | 1.15 | 16.3
0.6 | 1.04 | 9.5
0.707 | 1.00 | 4.3
Notes: Large Mr corresponds to large overshoot: both depend only on zeta.

## Slide 5: Other correlations
U3
Bandwidth and speed
ωb ∝ ωn, so tr ∝ 1/ωb: larger bandwidth gives smaller rise time.
ωr and tp
tp = π/ωd, and ωr ≈ ωn√(1 − 2ζ²): larger ωr gives smaller peak time.
Settling
ts = 4/(ζωn): a large ωn (large bandwidth) or damping gives a small ts.
Notes: Mr gives relative stability, bandwidth gives speed.

## Slide 6: Phase margin and damping ratio
U3
ζ | Phase margin PM (°) | Rule of thumb PM ≈ 100 ζ
0.2 | 22.6 | 20
0.4 | 43.1 | 40
0.6 | 59.2 | 60
0.707 | 65.5 | 70
Exact: PM = tan⁻¹ { 2ζ / √[ √(1 + 4ζ⁴) − 2ζ² ] }
Notes: Phase margin directly indicates the damping of the closed loop system.

## Slide 7: Numerical: use of correlation
U3
Problem A unity-feedback system must have Mp ≤ 16 %. Estimate the required ζ, Mr limit and phase margin.
Mp = 16 %: ζ ≈ 0.5
Mr = 1/(2ζ√(1 − ζ²)) = 1/(2 × 0.5 × 0.866) = 1.155 (1.25 dB)
PM = tan⁻¹ [1/√(√1.25 − 0.5)] = tan⁻¹(1.272)
Answer: ζ ≈ 0.5, Mr ≈ 1.15, PM ≈ 52°
Notes: These numbers translate a time domain specification into a frequency domain design target.

## Slide 8: Key takeaways
U3
Mr and Mp both depend only on ζ
tr ∝ 1/ωb; larger bandwidth = faster response
PM ≈ 100 ζ for ζ < 0.6
Use frequency plots to predict the transient behaviour
Notes: To summarise this topic. Mr and Mp both depend only on ζ. tr ∝ 1/ωb; larger bandwidth = faster response. PM ≈ 100 ζ for ζ < 0.6. Use frequency plots to predict the transient behaviour.

## Slide 9: Practice questions
U3
Q1. Find Mr for Mp = 25 %.
Q2. Why does a large bandwidth reduce rise time?
Q3. PM = 45°: estimate ζ and Mp.
Q4. Tabulate ζ, Mr, Mp for ζ = 0.2, 0.5.
Notes: Attempt these on your own, then check your working against your notes and textbook. Find Mr for Mp = 25 %. Why does a large bandwidth reduce rise time? PM = 45°: estimate ζ and Mp. Tabulate ζ, Mr, Mp for ζ = 0.2, 0.5.