## Slide 1
UNIT 3 · 7 hours
Gain Margin and Phase Margin
Frequency Domain Analysis
Control Systems (22EEG53)
Dr. Mitesh Astik · Dept. of Electrical and Electronics Engineering
NMAM Institute of Technology, Nitte · 2025-26
Notes: Welcome. In this session we study "Gain Margin and Phase Margin", part of Unit 3 (Frequency Domain Analysis) of Control Systems.

## Slide 2: Learning objectives
U3
Define gain and phase crossover frequencies
Define gain margin and phase margin
Determine margins from a Bode plot and analytically
Assess stability from margins
Syllabus context
Frequency domain analysis: frequency domain specifications peak resonance, resonant frequency, bandwidth and cut-off rate; correlation between time and frequency responses for second-order systems; Bode plot, gain margin and phase margin.
Notes: By the end of this topic you should be able to do the following. Define gain and phase crossover frequencies. Define gain margin and phase margin. Determine margins from a Bode plot and analytically. Assess stability from margins.

## Slide 3: Definitions
U3
Gain crossover ωgc
Frequency at which |G(jω)H(jω)| = 1 (0 dB).
Phase crossover ωpc
Frequency at which ∠GH = −180°.
GM and PM
PM = 180° + ∠GH(jωgc). GM = −20 log|GH(jωpc)| (dB), or 1/|GH(jωpc)|.
Stable closed loop (minimum phase): both GM and PM positive.
Notes: Gain margin is the additional gain that would bring the system to the verge of instability. Phase margin is the additional phase lag at gain crossover that would do so.

## Slide 4: Margins on the Bode plot
U3
G(s) = 2/[s(s+1)(s+2)].
ωgc = 0.75 rad/s: PM = 32.7°.
ωpc = 1.41 rad/s: GM = 9.5 dB.
Both positive ⇒ stable.
Notes: Read PM at the point where the magnitude crosses 0 dB, and GM at the point where the phase crosses minus one eighty degrees.

## Slide 5: Interpretation
U3
Condition | Meaning
GM > 0 dB and PM > 0° | Stable
GM = 0 dB and PM = 0° | Marginally stable (sustained oscillation)
GM < 0 dB or PM < 0° | Unstable
Good design | GM ≥ 6 dB (≥ 2×); PM = 30°–60°
Large PM | Well damped; small overshoot
Notes: A system that is conditionally stable needs more careful analysis.

## Slide 6: Numerical: margins analytically
U3
Problem G(s)H(s) = K/[s(s+1)(s+2)] with K = 2. Find ωpc, GM, ωgc and PM.
Phase = −90° − tan⁻¹ω − tan⁻¹(ω/2) = −180° ⇒ ω² = 2 ⇒ ωpc = 1.414 rad/s
|G(j1.414)| = 2/(1.414 × √3 × √6) = 2/6 = 1/3 ⇒ GM = 20 log 3 = 9.54 dB
|G| = 1 at ωgc = 0.748 rad/s; phase = −90 − 36.8 − 20.5 = −147.3°
PM = 180 − 147.3
Answer: GM = 9.54 dB, PM = 32.7°
Notes: The gain can be increased three times (to K = 6) before instability.

## Slide 7: Using the margins in design
U3
Gain K shifts the magnitude curve up/down without changing the phase: PM and GM change.
To get the required PM: find ω where phase = −180° + PM and set |G| = 1 there to fix K.
Phase margin ≈ 100 ζ links to the transient overshoot.
Compensators (Unit 5) reshape the Bode plot to meet GM and PM.
Notes: Margins are the safety allowance against model errors and parameter drift.

## Slide 8: Key takeaways
U3
ωgc: |GH| = 1; ωpc: ∠GH = −180°
PM = 180° + ∠GH(ωgc); GM = −20 log|GH(ωpc)|
Stable if GM > 0 dB and PM > 0°
Typical design: GM ≥ 6 dB, PM 30–60°
Notes: To summarise this topic. ωgc: |GH| = 1; ωpc: ∠GH = −180°. PM = 180° + ∠GH(ωgc); GM = −20 log|GH(ωpc)|. Stable if GM > 0 dB and PM > 0°. Typical design: GM ≥ 6 dB, PM 30–60°.

## Slide 9: Practice questions
U3
Q1. Define GM and PM and state the stability conditions.
Q2. For K/[s(s+1)(s+2)] find K for marginal stability.
Q3. Find PM for G = 10/[s(s+2)].
Q4. Explain how changing K changes the margins.
Notes: Attempt these on your own, then check your working against your notes and textbook. Define GM and PM and state the stability conditions. For K/[s(s+1)(s+2)] find K for marginal stability. Find PM for G = 10/[s(s+2)]. Explain how changing K changes the margins.